## Slide 1: ALTO Multi-Domain Use Cases and Services
Mario Lassnig, Ingmar Poese, Jordi Ros Giralt, Y. Richard Yang, Danny Lachos, Chin Guok
March 27, 2023
IETF 116
Notes: Need to get feedback from Sebastian Kiesel (U. Stuttgart)

## Slide 2: Problem (Relevance)
RFC 7971: "The ALTO protocol is designed for use cases where the ALTO server and client can be located in different organizations or trust domains. ALTO is inherently designed for use in multi-domain environments. Most importantly, ALTO is designed to enable deployments in which the ALTO server and the ALTO client are not located within the same administrative domain. ”
However, existing core ALTO services including Endpoint Cost Service (ECS) and Cost Map Service query a single ALTO server for the ALTO properties (e.g., routing cost, latency, …) of the whole network path, but the path may span multiple networks.
Notes: Multiple projects (e.g., [1][2]) identify systematic multi-domain design as a key missing feature of ALTO.
[1] https://datatracker.ietf.org/doc/draft-lachos-alto-multi-domain-use-cases/ [2] https://datatracker.ietf.org/doc/draft-xiang-alto-multidomain-analytics/

## Slide 3: Use Case Driven by Deployment: Multi-Domain Path->Link Usage (Example: CERN FTS Scheduling Integration)
AS 1
AS 2
AS 3
pipe[i].src
pipe[i].dst
Multi-domain applications
App controls transfer pipe traversing a set of resources
Each resource (link) has resource allocation model
App supporting app-defined-networking need the ability to map pipe to the set of resources
More detail see CERN ALTO/FTS integration.
Link 1.1
Link 3.1
project
activity
pipe

## Slide 4: Use Case Driven by Deployment: Multi-domain Path Distance/Ranking (Example: Rucio Distance/Flow Director)
Node X
Node 1A
Node 1B
Node 2B
Node 3B
Node 3A
Node 2A
Node X has 6 potential sources, Node [1-3]A, Node [1-3]B
Sources span multiple domains
How to compute distance/ranking for Node X?

## Slide 5: Use Case: Multi-domain Co-Flow Resource Discovery (Example: AutoGOLE/SENSE)
"Fine-grained, multi-domain network resource abstraction as a fundamental primitive to enable high-performance, collaborative data sciences." ACM/IEEE Supercomputing 2018.
Large-scale data analytics jobs span multiple networks
Compute QoS (possible bandwidth) to optimize co-flow finishing time
Notes: The multi-domain networking abstraction is used to solve application-layer optimizations across multiple domains.
Typically, previous uses cases ca be modeled as an optimization problem F(x, y) where the F is an objective function based on two types of variables.

## Slide 6: Additional Use Case
Multi-domain bottleneck structure
Details see https://datatracker.ietf.org/doc/draft-giraltyellamraju-alto-bsg-multidomain/

## Slide 7: Gap in Current ALTO/Routing Systems
For the same (src-dst) flow path,
  upstream sees more domains, e.g.,
    AS S can see the whole AS path S A B D; AS A sees only A B D
  upstream does not notify downstream egress (corresponding ingress at downstream)
    AS A does not know (by protocol) AS S chooses se1->ai1 or se2->ai2
    BGP does not have a CHOSEN message; ALTO has no resource to provide the info
AS S AS A AS B AS D
+-------------+se1 +---------+ +-----+ +------------+
| src --|-----|ai1 ae1|---| |---|di1 dst |
|+--+ --/ | | | | | | +--+ |
|| | --/ | | | | | | | | |
|+--+ \ |se2 | | | | | +--+ |
| \__ |_____|ai2 ae2|---| |---|di2 |
+-------------+ +---------+ +-----+ +------------+

## Slide 8: Feasibility: Basic ALTO Extension
Egress-notification resource (EN)
  <flow-info, ingress> -> <egress, domid:next-ingress; [Sebastian proposal: next-alto-server-uri; handle blackhole…]>
Useful beyond ALTO (egress/ingress verification)
An east-west interface between ALTO/AS
AS S AS A AS B AS D
+-------------+se1 +---------+ +-----+ +------------+
| src --|-----|ai1 ae1|---| |---|di1 dst |
|+--+ --/ | | | | | | +--+ |
|| | --/ | | | | | | | | |
|+--+ \ |se2 | | | | | +--+ |
| \__ |_____|ai2 ae2|---| |---|di2 |
+-------------+ +---------+ +-----+ +------------+

## Slide 9: Multidomain Endpoint Cost Service using EN
Option 1 (Horizontal)
  ALTO server coordination: Downstream queries upstream for ingress point (can detect anyway; but protocol convey intent, not error, before traffic)
Option 2 (Vertical)
  ALTO client provides upstream info to downstream
AS S AS A AS B AS D
+-------------+se1 +---------+ +-----+ +------------+
| src --|-----|ai1 ae1|---| |---|di1 dst |
|+--+ --/ | | | | | | +--+ |
|| | --/ | | | | | | | | |
|+--+ \ |se2 | | | | | +--+ |
| \__ |_____|ai2 ae2|---| |---|di2 |
+-------------+ +---------+ +-----+ +------------+

## Slide 10: Important Technical Detail: Trust Model
AS 2
AS 3
AS 1
Option 1: Horizontal trust
Client
Option 2: Star trust

## Slide 11: Important Technical Detail: Incremental Deployment
Incremental deployment: the chaining of domains may be broken due to incremental deployment (e.g., domain sequence is S -> A -> B -> C -> D, but A does not provide EN)
  Provide guidance on
    how to detect ingress point at B, and
    how to respond if B cannot detect ingress (multi-answers)
      See general path abstraction discussion on the mailing list

## Slide 12: Important Technical Detail: Multi-Domain Path Ranking
The multi-domain path of a flow from a src to a dst consists of those of a sequence of domain segments
    domain[0]:{src -> dom0-egress-> dom1-ingress} domain[i]{domi-ingress -> domi-egress -> domi+1-egress}
      src = dom0-ingress, dst = domn-egress
    List of domains obtained from BGP at source by default => bootstrapping starts at source
A vector of path cost may no longer define a total order; candidate designs MUST discuss clear guidelines to applications on how to utilize partial ordering, and the consequences (i.e., operations considerations)
  Leverage SIGCOMM’20 multi-criteria routing design
src
dst
dom0-egress
dom1-ingress
Notes: Same network: segment-src-dst
One hop: segment–src -> segment-dst

## Slide 13: Related References on Multidomain
https://datatracker.ietf.org/doc/draft-lachos-alto-multi-domain-use-cases/
https://datatracker.ietf.org/doc/draft-lachos-sfc-multi-domain-alto/
https://datatracker.ietf.org/doc/draft-lachosrothenberg-alto-brokermdo/
https://datatracker.ietf.org/doc/draft-lachosrothenberg-alto-md-e2e-ns/
Latest CERN use case: TCN
Old CERN use case
  https://ieeexplore.ieee.org/abstract/document/8756056
  https://www.sciencedirect.com/science/article/abs/pii/S0167739X18302413
Inter-ALTO communication protocol
  https://datatracker.ietf.org/doc/draft-dulinski-alto-inter-alto-protocol/
ALTO network-server, server-server API
  https://datatracker.ietf.org/doc/draft-medved-alto-svr-apis/

## Slide 14: Next Steps
Organizing interim meetings before May 2023
  Discuss details of current design implementations
  Involve operators
Notes: Extensions of ALTO services to support multi-domain settings. The current ALTO framework has made clear how to provide network information from a single ALTO server for a single network (administrative domain), but the network devices traversed by a flow can be managed by multiple networks that are not in the same domain. The working group will investigate and extend the ALTO framework to (1) specify multi-ALTO-server protocol flow and usage guidelines when an ALTO service involves network paths spanning multiple domains with multiple ALTO servers, and (2) extend or introduce ALTO services allowing east-west interfaces for multiple ALTO server integration and collaboration. The specification and extensions should use existing services whenever possible. The specification and extensions should consider realistic complexities including incremental deployment, dynamicity, and security issues including access control, authorization (e.g., an ALTO server provides information for a network that the server has no authorization), and privacy protection in multi-domain settings.

## Slide 15: Backup Slides

## Slide 16: Additional Questions
The “routing cost” metric makes it difficult to aggregate different point of views
  See also RFC 8686, Appendix C
The “ALTO advice” runs in the opposite direction of the money
  will it always stop at the peering points / Tier-1 carriers?
  what if the advice given by ISP1’s ALTO server impairs ISP2’s traffic engineering?
  will ISP1 be legally liable? Thus, will ISP1 refuse to give details wrt. ISP2 even if they knew?
[Sebastian 9/30/2020]

## Slide 17: (R)PV: Mathematical Programming as Abstraction Representation to Support Third Use Case
100
100
Redundant inequalities can be removed via a polynomial-time, optimal algorithm.
Remaining bottlenecks represented as abstract network elements (ANE).
GOAL: Use mathematical programming constraints to provide a compact representation of the available bandwidth of flows through a network.
Notes: Our idea: on-demand, partianl-instantiation

## Slide 18: The Reverse View: Mathematical Constraints as Virtual Network Representation
Aggregate the abstraction in multiple networks into a unified, single, virtual representation:

## Slide 19: Use Case: Multi-domain Path Distance/Ranking (Cost Map/Flow Director/Rucio Distance)
Node1A
Node 1 B
Node 2A, 2B (*)
Node 3A, 3B (*)
Node 1A
Node 2A, 2B (*)
Node1B
Node3A, 3B (*)
Is “all within my domain” or “not in my
wireless network” more preferable?
Node X
Node 1A
Node 1B
Node 2B
Node 3B
Node 3A
Node 2A
(*) = ?A and ?B are on the same level of preference, because ISP1 might not know that they are wireline vs. wireless, doesn’t care (monetary cost is the same for ISP1), and/or wouldn’t dare to tell even if they knew.
Which distance/ranking should Node X receive?

## Slide 20: Feasibility: Simple ALTO Multi-Domain Abstraction
Starts with a simple architecture called ALTO Multi-Domain Abstractions (AMDA)
  The path of a flow from a src to a dst consists of a sequence (vector) of domain segments
    Domain[0]:{src -> net0-e} -> Domain[i]{neti-i -> … -> neti-e -> neti+1-i -> … -> netn-e -> dst
    Domain segments obtained from BGP at source => bootstrapping starts at source
src
dst
net0-e
net1-i
netn-e
Notes: Same network: segment-src-dst
One hop: segment–src -> segment-dst

## Slide 21: Gap in Current ALTO/Routing Systems
Missing standard protocol to stitch information across domains
  Take computing cost/distance src->dst as an example
    AS S alone has complete path property, but only for BGP path
    AS S and AS D together can provide only distance from endpoints (e.g., GeoIP)
    AS A/B in the middle can provide path segments, if it can detect/determine ingress point (not common for downstream to know)
      Gap: provide an ability to provide ingress point from upstream
AS S AS A AS B AS D
+-------------+se1 +---------+ +-----+ +------------+
| src --|-----|ai1 ae1|---| |---|di1 dst |
|+--+ --/ | | | | | | +--+ |
|| | --/ | | | | | | | | |
|+--+ \ |se2 | | | | | +--+ |
| \__ |_____|ai2 ae2|---| |---|di2 |
+-------------+ +---------+ +-----+ +------------+

## Slide 22: Additional Issues
Operation models for extensions [mechanisms, not policies]
  iterative (client aggregation)
  recursive (network helped aggregation)
  Hybrid
How to handle cost map, not only ECS
How to handle bandwidth use case