## Slide 1: ALTO Multi-Domain Use Cases and Services
Presenter: authors
March 27, 2023
IETF 116
Notes: Sebastian Kiesel (U. Stuttgart)
Ingmar Poese (Benocs) Y. Richard Yang (Yale U.)
Chin Guok (esnet)
Danny

## Slide 2: Problem (Relevance)
RFC 7971: "The ALTO protocol is designed for use cases where the ALTO server and client can be located in different organizations or trust domains. ALTO is inherently designed for use in multi-domain environments. Most importantly, ALTO is designed to enable deployments in which the ALTO server and the ALTO client are not located within the same administrative domain. ”
However, existing core ALTO services including Endpoint Cost Service (ECS) and Cost Map Service query a single ALTO server for the ALTO properties (e.g., routing cost, latency, …) of the whole network path, but the path may span multiple networks served by multiple ALTO servers.
Notes: Multiple projects (e.g., [1][2]) identify systematic multi-domain design as a key missing feature of ALTO.
[1] https://datatracker.ietf.org/doc/draft-lachos-alto-multi-domain-use-cases/ [2] https://datatracker.ietf.org/doc/draft-xiang-alto-multidomain-analytics/

## Slide 3: Use Case Driven by Deployment: Multi-Domain Path->Link Usage (Example: CERN FTS Scheduling Integration)
Given src/dst, identify if the path traverses resource-control links
AS 1
AS 2
AS 3
pipe[i].src
pipe[i].dst
The goal is to control the amount of traffic on Link 1.1 and Link 3.1
For proper accounting, need to know if pipe[i].src->pipe[2].dst uses which link(s)
More detail see CERN ALTO/FTS integration.
Link 1.1
Link 3.1

## Slide 4: Use Case Driven by Deployment: Multi-domain Path Distance/Ranking (Example: Flow Director/Rucio Distance)
Node X
Node 1A
Node 1B
Node 2B
Node 3B
Node 3A
Node 2A
Which distance/ranking should Node X receive?

## Slide 5: Use Case: Multi-domain Co-Flow Resource Discovery (Example: AutoGole/SENSE)
"Fine-grained, multi-domain network resource abstraction as a fundamental primitive to enable high-performance, collaborative data sciences." ACM/IEEE Supercomputing 2018.
Large-scale data analytics span multiple networks.
Bottlenecks can come from multiple networks
Ideally, the networks collaborate but operate independently as much as possible.
Identify available bandwidth across multiple networks
Notes: The multi-domain networking abstraction is used to solve application-layer optimizations across multiple domains.
Typically, previous uses cases ca be modeled as an optimization problem F(x, y) where the F is an objective function based on two types of variables.

## Slide 6: Add Bottleneck Structure or Keep Simple?

## Slide 7: Feasibility: Simple ALTO Multi-Domain Abstraction
Starts with a simple architecture called ALTO Multi-Domain Abstractions (AMDA)
  The path of a flow from a src to a dst consists of a sequence (vector) of segments from multiple networks
    src -> net1-e -> net2-i -> … -> neti-e -> neti+1-i -> … -> netn-e -> dst
  Segments obtained from BGP at source, bootstrapping starts at source [already implemented]
  The cost of a path is a vector corresponding to the vector of segments
  The paths of a set of flows form a flow graph
    Constructed by merging shared egress or ingress nodes of the segments
src
dst
net1-e
net2-i
netn-e

## Slide 8: ALTO Extensions to Realize AMDA
Ext 1: Segment discovery (to support flow->link use case) [implemented]
  <flow, netid:ingress> -> <netid:egress, netid:next-ingress; [Sebastian proposal: next-alto-server-uri; handle blackhole…]>
Ext 2: Path cost discovery (extend ECS/cost map service, supporting ranking use case)
  <segment-set, metric> -> <cost/metric>
Operation models for extensions [mechanisms, not policies]
  iterative (client aggregation)
  recursive (network helped aggregation)
  hybrid

## Slide 9: Important Technical Detail: Incremental Deployment
Incremental deployment: the chaining of domains may be broken due to incremental deployment (e.g., domain sequence is S -> A -> B -> C -> D, but A does not provide AMDA)
  Need to detect ingress point at B
  Need to provide multi-path when detection is not unique
    See general path abstraction discussion on the mailing list

## Slide 10: Important Technical Detail: ADMA Ranking
A vector of path cost may no longer defines a total order; candidate designs MUST discuss clear guidelines to applications on how to utilize partial ordering, and the consequences (i.e., operations considerations)
  Leverage SIGCOMM’20 multi-criteria routing design

## Slide 11: Important Technical Detail: Discuss Trust Model
Discuss implications of revealing egress points
Discuss star vs chaining trust models
AS 2
AS 3
AS 1
Horizontal trust (to allow recursive)
Client
Star trust model

## Slide 12: Related References on Multidomain
https://datatracker.ietf.org/doc/draft-lachos-alto-multi-domain-use-cases/
https://datatracker.ietf.org/doc/draft-lachos-sfc-multi-domain-alto/
https://datatracker.ietf.org/doc/draft-lachosrothenberg-alto-brokermdo/
https://datatracker.ietf.org/doc/draft-lachosrothenberg-alto-md-e2e-ns/
CERN use case
  https://ieeexplore.ieee.org/abstract/document/8756056
  https://www.sciencedirect.com/science/article/abs/pii/S0167739X18302413
Inter-ALTO communication protocol
  https://datatracker.ietf.org/doc/draft-dulinski-alto-inter-alto-protocol/
ALTO network-server, server-server API
  https://datatracker.ietf.org/doc/draft-medved-alto-svr-apis/

## Slide 13: Backup Slides

## Slide 14: Additional Questions
The “routing cost” metric makes it difficult to aggregate different point of views
  See also RFC 8686, Appendix C
The “ALTO advice” runs in the opposite direction of the money
  will it always stop at the peering points / Tier-1 carriers?
  what if the advice given by ISP1’s ALTO server impairs ISP2’s traffic engineering?
  will ISP1 be legally liable? Thus, will ISP1 refuse to give details wrt. ISP2 even if they knew?
[Sebastian 9/30/2020]

## Slide 15: (R)PV: Mathematical Programming as Abstraction Representation to Support Third Use Case
100
100
Redundant inequalities can be removed via a polynomial-time, optimal algorithm.
Remaining bottlenecks represented as abstract network elements (ANE).
GOAL: Use mathematical programming constraints to provide a compact representation of the available bandwidth of flows through a network.
Notes: Our idea: on-demand, partianl-instantiation

## Slide 16: The Reverse View: Mathematical Constraints as Virtual Network Representation
Aggregate the abstraction in multiple networks into a unified, single, virtual representation:

## Slide 17: One Paragraph
Extensions of ALTO services to support multi-domain settings. The current ALTO framework has made clear how to provide network information from a single ALTO server for a single network (administrative domain), but the network devices traversed by a flow can be managed by multiple networks that are not in the same domain. The working group will investigate and extend the ALTO framework to (1) specify multi-ALTO-server protocol flow and usage guidelines when an ALTO service involves network paths spanning multiple domains with multiple ALTO servers, and (2) extend or introduce ALTO services allowing east-west interfaces for multiple ALTO server integration and collaboration. The specification and extensions should use existing services whenever possible. The specification and extensions should consider realistic complexities including incremental deployment, dynamicity, and security issues including access control, authorization (e.g., an ALTO server provides information for a network that the server has no authorization), and privacy protection in multi-domain settings.

## Slide 18: Use Case: Multi-domain Path Distance/Ranking (Cost Map/Flow Director/Rucio Distance)
Node1A
Node 1 B
Node 2A, 2B (*)
Node 3A, 3B (*)
Node 1A
Node 2A, 2B (*)
Node1B
Node3A, 3B (*)
Is “all within my domain” or “not in my
wireless network” more preferable?
Node X
Node 1A
Node 1B
Node 2B
Node 3B
Node 3A
Node 2A
(*) = ?A and ?B are on the same level of preference, because ISP1 might not know that they are wireline vs. wireless, doesn’t care (monetary cost is the same for ISP1), and/or wouldn’t dare to tell even if they knew.
Which distance/ranking should Node X receive?